## Slide 1
Chapter 3 – Chip Planning

## Slide 2: Chapter 3 – Chip Planning
3.1 Introduction to Floorplanning
3.2 Optimization Goals in Floorplanning
3.3 Terminology
3.4 Floorplan Representations
  3.4.1 Floorplan to a Constraint-Graph Pair
  3.4.2 Floorplan to a Sequence Pair
  3.4.3 Sequence Pair to a Floorplan
3.5 Floorplanning Algorithms
  3.5.1 Floorplan Sizing
  3.5.2 Cluster Growth
  3.5.3 Simulated Annealing
  3.5.4 Integrated Floorplanning Algorithms
3.6 Pin Assignment
3.7 Power and Ground Routing
  3.7.1 Design of a Power-Ground Distribution Network
  3.7.2 Planar Routing
  3.7.3 Mesh Routing

## Slide 3: 3.1 Introduction
ENTITY test is port a: in bit; end ENTITY test;
DRC LVS
ERC
Circuit Design
Functional Design and Logic Design
Physical Design
Physical Verification and Signoff
Fabrication
System Specification
Architectural Design
Chip
Packaging and Testing
Chip Planning
Placement
Signal Routing
Partitioning
Timing Closure
Clock Tree Synthesis

## Slide 4: 3.1 Introduction
GND
VDD
Module e
I/O Pads
Block Pins
Block a
Block b
Block d
Block e
Floorplan
Module d
Module c
Module b
Module a
Chip Planning
Block c
Supply Network
© 2022 Springer Verlag

## Slide 5: 3.1 Introduction
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed
A
A
A
B
B
C
C

## Slide 6: 3.1 Introduction
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed

## Slide 7: 3.1 Introduction
Solution:
Aspect ratios Block A with w = 2, h = 2; Block B with w = 2, h = 1; Block C with w = 1, h = 3
This floorplan has a global bounding box with minimum possible area (9 square units).
Example
Given: Three blocks with the following potential widths and heights
Block A: w = 1, h = 4 or w = 4, h = 1 or w = 2, h = 2
Block B: w = 1, h = 2 or w = 2, h = 1
Block C: w = 1, h = 3 or w = 3, h = 1
Task: Floorplan with minimum total area enclosed

## Slide 8: 3.2 Optimization Goals in Floorplanning
Area and shape of the global bounding box
  Global bounding box of a floorplan is the minimum axis-aligned rectangle that contains all floorplan blocks.
  Area of the global bounding box represents the area of the top-level floorplan
  Minimizing the area involves finding (x,y) locations, as well as shapes, of the individual blocks.
Total wirelength
  Long connections between blocks may increase signal propagation delays in the design.
Combination of area area(F) and total wirelength L(F) of floorplan F
  Minimize  ∙ area(F) + (1 – ) ∙ L(F) where the parameter 0 ≤  ≤ 1 gives the relative importance between area(F) and L(F)
Signal delays
  Static timing analysis is used to identify the interconnects that lie on critical paths.

## Slide 9: 3.3 Terminology
A rectangular dissection is a division of the chip area into a set of blocks or non-overlapping rectangles.
A slicing floorplan is a rectangular dissection
  Obtained by repeatedly dividing each rectangle, starting with the entire chip area, into two smaller rectangles
  Horizontal or vertical cut line.
A slicing tree or slicing floorplan tree is a binary tree with k leaves and k – 1 internal nodes
  Each leaf represents a block
  Each internal node represents a horizontal or vertical cut line.

## Slide 10: 3.3 Terminology
Slicing floorplan and two possible corresponding slicing trees
b
d
a
e
c
f
a
c
b
d
e
f
H
V
H
H
V
H
V
H
d
c
e
f
H
V
b
a

## Slide 11: 3.3 Terminology
Polish expression
b
d
a
e
c
f
a
c
b
d
e
f
H
V
H
H
V
B
+
C

A
D
E
F

+
+
Bottom up: V   and H  +
Length 2n-1 (n = Number of leaves of the slicing tree)

## Slide 12: 3.3 Terminology
Non-slicing floorplans (wheels)
b
d
a
e
c
a
b
c
d
e

## Slide 13: 3.3 Terminology
Floorplan tree: Tree that represents a hierarchical floorplan
a
b
c
d
e
f
g
h
i
H
H
H
H
V
W
h
i
c
d
e
f
g
a
b
H
H
Horizontal division (objects to the top and bottom)
H
V
Vertical division (objects to the left and right)
H
W
Wheel (4 objects cycled around a center object)
© 2022 Springer Verlag

## Slide 14: 3.3 Terminology
In a vertical constraint graph (VCG), node weights represent the heights of the corresponding blocks.
  Two nodes vi and vj, with corresponding blocks mi and mj, are connected with a directed edge from vi to vj if mi is below mj.
In a horizontal constraint graph (HCG), node weights represent the widths of the corresponding blocks.
  Two nodes vi and vj, with corresponding blocks mi and mj, are connected with a directed edge from vi to vj if mi is to the left of mj.
The longest path(s) in the VCG / HCG correspond(s) to the minimum vertical / horizontal floorplan span required to pack the blocks (floorplan height / width).
A constraint-graph pair is a floorplan representation that consists of two directed graphs – vertical constraint graph and horizontal constraint graph – which capture the relations between block positions.

## Slide 15: 3.3 Terminology
Constraint graphs
Horizontal Constraint Graph
Vertical Constraint Graph
a
b
c
d
e
f
g
h
i
e
h
i
d
g
b
c
f
a
s
t
a
b
h
i
s
g
f
c
d
e
t
© 2022 Springer Verlag

## Slide 16: 3.3 Terminology
Sequence pair
Two permutations represent geometric relations between every pair of blocks
Example: (ABDCE, CBAED)
Horizontal and vertical relations between blocks A and B:
  (… A … B … , … A … B …) → A is left of B
  (… A … B … , … B … A …) → A is above B
  (… B … A … , … A … B …) → A is below B
  (… B … A … , … B … A …) → A is right of B
C
A
B
D
E

## Slide 17: 3.4 Floorplan Representations
17
3.1 Introduction to Floorplanning
3.2 Optimization Goals in Floorplanning
3.3 Terminology
3.4 Floorplan Representations
  3.4.1 Floorplan to a Constraint-Graph Pair
  3.4.2 Floorplan to a Sequence Pair
  3.4.3 Sequence Pair to a Floorplan
3.5 Floorplanning Algorithms
  3.5.1 Floorplan Sizing
  3.5.2 Cluster Growth
  3.5.3 Simulated Annealing
  3.5.4 Integrated Floorplanning Algorithms
3.6 Pin Assignment
3.7 Power and Ground Routing
  3.7.1 Design of a Power-Ground Distribution Network
  3.7.2 Planar Routing
  3.7.3 Mesh Routing

## Slide 18: 3.4.1 Floorplan to a Constraint-Graph Pair
Create nodes for every block
In addition, create a source node and a sink one
18
a
c
d
e
s
t
b
a
c
d
e
b

## Slide 19: 3.4.1 Floorplan to a Constraint-Graph Pair
Create nodes for every block.
In addition, create a source node and a sink one.
Add a directed edge (A,B) if Block A is below/left of Block B. (HCG)
19
a
c
d
e
s
t
b
a
c
d
e
b

## Slide 20: 3.4.1 Floorplan to a Constraint-Graph Pair
Create nodes for every block.
In addition, create a source node and a sink one.
Add a directed edge (A,B) if Block A is below/left of Block B. (HCG)
Remove the redundant edges that can be derived from other edges by transitivity.
20
a
c
d
e
s
t
b
a
c
d
e
b

## Slide 21: 3.4.2 Floorplan to a Sequence Pair
21
Given two blocks A and B with
  Locations: A = (xA,yA) and B = (xB,yB)
  Dimensions: A = (wA,hA) and B = (wB,hB)
If and or , then A is left of B
If and or , then A is below B
a
c
d
e
b

## Slide 22: 3.4.3 Sequence Pair to a Floorplan
22
Start with the bottom left corner
Define a weighted sequence as a sequence of blocks based on width
  Each block B has its own width w(B)
Old (traditional) algorithm: find the longest path through edges (O(n2))
Newer approach: find the longest common subsequence (LCS)
  Given two weighted sequences S1 and S2, the LCS(S1,S2) is the longest sequence found in both S1 and S2
  The length of LCS(S1,S2) is the sum of weights
For block placement:
  LCS(S+,S-) returns the x-coordinates of all blocks
  LCS(S+R,S-) returns the y-coordinates of all blocks (S+R is the reverse of S+)
  The length of LCS(S+,S-) and LCS(S+R,S-) is the width and height, respectively

## Slide 23: 3.4.3 Sequence Pair to a Floorplan
23
Algorithm: Longest Common Subsequence (LCS)
Input: sequences S1 and S2, weights of n blocks weights
Output: positions of each block positions, total span L
for (i = 1 to n) // initialization
block_order[S2[i]] = i
lengths[i] = 0
for (i = 1 to n)
block = S1[i] // current block
index = block_order[block]
positions[block] = lengths[index] // compute block position
t_span = positions[block] + weights[block] // finds length of sequence // from beginning to block
for (j = index to n) // update total length
if (t_span > lengths[j]) lengths[j] = t_span
else break
L = lengths[n] // total length is stored here

## Slide 24: 3.4.3 Sequence Pair to a Floorplan
24
Example: S1 = <acdbe>, S2 = <cdaeb>, widths[a b c d e] = [8 4 4 4 4], heights[a b c d e] = [4 2 5 5 6]
Find x-coordinates – go by S1’s order:
Initial: block_order[a b c d e] = [3 5 1 2 4], lengths = [0 0 0 0 0]
Iteration 1 – block = a, index = 3: positions[a] = lengths[3] = 0, t_span = 8, lengths = [0 0 8 8 8]
Iteration 2 – block = c, index = 1: positions[c] = lengths[1] = 0, t_span = 4, lengths = [4 4 8 8 8]
Iteration 3 – block = d, index = 2: positions[d] = lengths[2] = 4, t_span = 8, lengths = [4 8 8 8 8]
Iteration 4 – block = b, index = 5: positions[b] = lengths[5] = 8, t_span = 12, lengths = [4 8 8 8 12]
Iteration 5 – block = e, index = 4: positions[e] = lengths[4] = 8, t_span = 12, lengths = [4 8 8 12 12]
positions[a b c d e] = [0 8 0 4 8], total_width = lengths[n = 5] = 12

## Slide 25: 3.4.3 Sequence Pair to a Floorplan
25
Example: S1 = <acdbe>, S2 = <cdaeb>, widths[a b c d e] = [8 4 4 4 4], heights[a b c d e] = [4 2 5 5 6]
Find y-coordinates – go by S1R’s order:
Initial: block_order[a b c d e] = [3 5 1 2 4], lengths = [0 0 0 0 0]
Iteration 1 – block = e, index = 4: positions[e] = lengths[4] = 0, t_span = 6, lengths = [0 0 0 6 6]
Iteration 2 – block = b, index = 5: positions[b] = lengths[5] = 6, t_span = 9, lengths = [0 0 0 6 9]
Iteration 3 – block = d, index = 2: positions[d] = lengths[2] = 0, t_span = 5, lengths = [0 5 5 6 9]
Iteration 4 – block = c, index = 1: positions[c] = lengths[1] = 0, t_span = 5, lengths = [5 5 5 6 9]
Iteration 5 – block = a, index = 3: positions[a] = lengths[3] = 5, t_span = 9, lengths = [5 5 9 9 9]
positions[a b c d e] = [5 6 0 0 0], total_height = lengths[n = 5] = 9

## Slide 26: 3.5 Floorplanning Algorithms
3.1 Introduction to Floorplanning
3.2 Optimization Goals in Floorplanning
3.3 Terminology
3.4 Floorplan Representations
  3.4.1 Floorplan to a Constraint-Graph Pair
  3.4.2 Floorplan to a Sequence Pair
  3.4.3 Sequence Pair to a Floorplan
3.5 Floorplanning Algorithms
  3.5.1 Floorplan Sizing
  3.5.2 Cluster Growth
  3.5.3 Simulated Annealing
  3.5.4 Integrated Floorplanning Algorithms
3.6 Pin Assignment
3.7 Power and Ground Routing
  3.7.1 Design of a Power-Ground Distribution Network
  3.7.2 Planar Routing
  3.7.3 Mesh Routing

## Slide 27: 3.5 Floorplanning Algorithms
27
Otten, R.: Efficient Floorplan Optimization. Int. Conf. on Computer Design, 499-502, 1983
Common Goals
To minimize the total length of interconnect, subject to an upper bound on the floorplan area
or
To simultaneously optimize both wire length and area

## Slide 28: 3.5.1 Floorplan Sizing
Shape functions
Legal shapes
Legal shapes
w
h
w
h
Block with minimum width and height restrictions
ha*aw  A
Otten, R.: Efficient Floorplan Optimization. Int. Conf. on Computer Design, 499-502, 1983

## Slide 29: 3.5.1 Floorplan Sizing
Shape functions
w
h
Hard library block
Otten, R.: Efficient Floorplan Optimization. Int. Conf. on Computer Design, 499-502, 1983
w
h
Discrete (h,w) values

## Slide 30: 3.5.1 Floorplan Sizing
Corner points
5
2
2
5
2
5
2
5
w
h

## Slide 31: 3.5.1 Floorplan Sizing
Algorithm
This algorithm finds the minimum floorplan area for a given slicing floorplan in
polynomial time. For non-slicing floorplans, the problem is NP-hard.
Construct the shape functions of all individual blocks
Bottom up: Determine the shape function of the top-level floorplan from the shape functions of the individual blocks
Top down: From the corner point that corresponds to the minimum top-level floorplan area, trace back to each block’s shape function to find that block’s dimensions and location.

## Slide 32: 3.5.1 Floorplan Sizing – Example
4
2
2
4
Block B:
Block A:
5
5
3
3
Step 1: Construct the shape functions of the blocks

## Slide 33: 3.5.1 Floorplan Sizing – Example
4
2
2
4
Block B:
Block A:
5
5
3
3
Step 1: Construct the shape functions of the blocks
2
4
h
6
w
2
6
4
5
3

## Slide 34: 3.5.1 Floorplan Sizing – Example
4
2
2
4
Block B:
Block A:
5
5
3
3
Step 1: Construct the shape functions of the blocks
2
4
h
w
2
6
4
6
3
5

## Slide 35: 3.5.1 Floorplan Sizing – Example
4
2
2
4
Block B:
Block A:
5
5
3
3
w
2
6
2
4
h
4
6
hA(w)
Step 1: Construct the shape functions of the blocks

## Slide 36: 3.5.1 Floorplan Sizing – Example
4
2
2
4
Block B:
Block A:
5
5
3
3
hB(w)
w
2
6
2
4
h
4
6
hA(w)
Step 1: Construct the shape functions of the blocks

## Slide 37: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
hB(w)
hA(w)
8
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 38: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
hB(w)
hA(w)
8
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 39: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
w
2
6
2
4
h
4
6
hB(w)
hA(w)
hB(w)
hA(w)
hC(w)
8
8
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 40: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
w
2
6
2
4
h
4
6
hB(w)
hA(w)
hB(w)
hA(w)
hC(w)
5 x 5
8
8
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 41: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
w
2
6
2
4
h
4
6
hB(w)
hA(w)
hB(w)
hA(w)
hC(w)
3 x 9
4 x 7
5 x 5
8
8
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 42: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
w
2
6
2
4
h
4
6
hB(w)
hA(w)
hB(w)
hA(w)
hC(w)
3 x 9
4 x 7
5 x 5
8
8
Minimimum top-level floorplan
with vertical composition
Step 2: Determine the shape function of the top-level floorplan (vertical)

## Slide 43: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
w
2
6
2
4
h
4
6
hA(w)
hB(w)
hC(w)
hA(w)
hB(w)
9 x 3
7 x 4
5 x 5
8
8
Step 2: Determine the shape function of the top-level floorplan (horizontal)
Minimimum top-level floorplan
with horizontal composition

## Slide 44: 3.5.1 Floorplan Sizing – Example
Step 3: Find the individual blocks’ dimensions and locations
w
2
6
2
4
h
4
6
8
(1) Minimum area floorplan: 5 x 5
Horizontal composition

## Slide 45: 3.5.1 Floorplan Sizing – Example
w
2
6
2
4
h
4
6
(1) Minimum area floorplan: 5 x 5
(2) Derived block dimensions : 2 x 4 and 3 x 5
8
Step 3: Find the individual blocks’ dimensions and locations
Horizontal composition

## Slide 46: 3.5.1 Floorplan Sizing – Example
2 x 4
3 x 5
5 x 5
Step 3: Find the individual blocks’ dimensions and locations
w
2
6
2
4
h
4
6
(1) Minimum area floorplan: 5 x 5
(2) Derived block dimensions : 2 x 4 and 3 x 5
8
Horizontal composition

## Slide 47: 3.5.1 Floorplan Sizing – Example
2 x 4
3 x 5
5 x 5
Resulting slicing tree
B
V
A
B
A

## Slide 48: 3.5.2 Cluster Growth
w
h
w
h
w
h
a
a
a
b
b
c
Growth direction
2
4
6
4
6
4
Iteratively add blocks to the cluster until all blocks are assigned
Only the different orientations of the blocks instead of the shape / aspect ratio are taken into account
Linear ordering to minimize total wirelength of connections between blocks
© 2022 Springer Verlag

## Slide 49: 3.5.2 Cluster Growth – Linear Ordering
New nets have no pins on any block from the partially-constructed ordering
Terminating nets have no other incident blocks that are unplaced
Continuing nets have at least one pin on a block from the partially-constructed ordering and at least one pin on an unordered block
…
Terminating nets
New nets
Continuing nets

## Slide 50: 3.5.2 Cluster Growth – Linear Ordering
Gain of each block m is calculated: Gainm = (Number of terminating nets of m) – (New nets of m)
The block with the maximum gain is selected to be placed next
A
B
N1
N4
GainB = 1 – 1 = 0

## Slide 51: 3.5.2 Cluster Growth – Linear Ordering (Example)
A
B
C
D
E
N1
N2
N3
N4
N5
N6

## Slide 52
A
B
C
D
E
N1
N2
N3
N4
N5
N6
--
2
N3,N5
--
C
4
N3,N5
N3,N5
0
1
--
N6
--
--
C
E
3
N3
--
N3
-1
0
-2
--
N2,N4
--
N5
N5,N6
N5,N6
C
D
E
2
--
N3
--
N3
0
-1
-2
-2
N1
--
N2
--
N4
N5
N4,N5,N6
N5,N6
B
C
D
E
1
--
-3
--
N1,N2,N3
A
0
Continuing Nets
Gain
Terminating Nets
New Nets
Block
Iteration #
A
B
D
E
C
N1
N2
N4
N5
N6
N3
GainA = (Number of terminating nets of A) – (New nets of A)
Initial block

## Slide 53
A
B
C
D
E
N1
N2
N3
N4
N5
N6
--
2
N3,N5
--
C
4
N3,N5
N3,N5
0
1
--
N6
--
--
C
E
3
N3
--
N3
-1
0
-2
--
N2,N4
--
N5
N5,N6
N5,N6
C
D
E
2
--
N3
--
N3
0
-1
-2
-2
N1
--
N2
--
N4
N5
N4,N5,N6
N5,N6
B
C
D
E
1
--
-3
--
N1,N2,N3
A
0
Continuing Nets
Gain
Terminating Nets
New Nets
Block
Iteration #
A
B
D
E
C
N1
N2
N4
N5
N6
N3

## Slide 54
A
B
C
D
E
N1
N2
N3
N4
N5
N6
--
2
N3,N5
--
C
4
N3,N5
N3,N5
0
1
--
N6
--
--
C
E
3
N3
--
N3
-1
0
-2
--
N2,N4
--
N5
N5,N6
N5,N6
C
D
E
2
--
N3
--
N3
0
-1
-2
-2
N1
--
N2
--
N4
N5
N4,N5,N6
N5,N6
B
C
D
E
1
--
-3
--
N1,N2,N3
A
0
Continuing Nets
Gain
Terminating Nets
New Nets
Block
Iteration #
A
B
D
E
C
N1
N2
N4
N5
N6
N3

## Slide 55
A
B
C
D
E
N1
N2
N3
N4
N5
N6
--
2
N3,N5
--
C
4
N3,N5
N3,N5
0
1
--
N6
--
--
C
E
3
N3
--
N3
-1
0
-2
--
N2,N4
--
N5
N5,N6
N5,N6
C
D
E
2
--
N3
--
N3
0
-1
-2
-2
N1
--
N2
--
N4
N5
N4,N5,N6
N5,N6
B
C
D
E
1
--
-3
--
N1,N2,N3
A
0
Continuing Nets
Gain
Terminating Nets
New Nets
Block
Iteration #
© 2022 Springer Verlag

## Slide 56: 3.5.2 Cluster Growth – Linear Ordering (Example)
A
B
D
E
C
N1
N2
N3
N4
N5
N6
A
B
C
D
E
N1
N2
N3
N4
N5
N6

## Slide 57: 3.5.2 Cluster Growth – Algorithm
Input: set of all blocks M, cost function C
Output: optimized floorplan F based on C
F = Ø
order = LINEAR_ORDERING(M) // generate linear ordering
for (i = 1 to |order|)
curr_block = order[i]
ADD_TO_FLOORPLAN(F,curr_block,C) // find location and orientation // of curr_block that causes // smallest increase based on
// C while obeying constraints

## Slide 58: 3.5.2 Cluster Growth
58
The objective is to minimize the total wirelength of connections blocks
Though this produces mediocre solutions, the algorithm is easy to implement and fast.
Can be used to find the initial floorplan solutions for iterative algorithms such as simulated annealing.
Analysis

## Slide 59: 3.5.3 Simulated Annealing
59
Simulated Annealing (SA) algorithms are iterative in nature.
Begins with an initial (arbitrary) solution and seeks to incrementally improve the objective function.
During each iteration, a local neighborhood of the current solution is considered. A new candidate solution is formed by a small perturbation of the current solution.
Unlike greedy algorithms, SA algorithms can accept candidate solutions with higher cost.
Introduction

## Slide 60: 3.5.3 Simulated Annealing
Solution states
Cost
Initial solution
Local optimum
Global optimum

## Slide 61: 3.5.3 Simulated Annealing
61
Definition (from material science): controlled cooling process of high-temperature materials to modify their properties.
Cooling changes material structure from being highly randomized (chaotic) to being structured (stable).
The way that atoms settle in low-temperature state is probabilistic in nature.
Slower cooling has a higher probability of achieving a perfect lattice with minimum-energy
  Cooling process occurs in steps
  Atoms need enough time to try different structures
  Sometimes, atoms may move across larger distances and create (intermediate) higher-energy states
  Probability of the accepting higher-energy states decreases with temperature
What is annealing?

## Slide 62: 3.5.3 Simulated Annealing
62
Generate an initial solution Sinit, and evaluate its cost.
Generate a new solution Snew by performing a random walk
Snew is accepted or rejected based on the temperature T
  Higher T means a higher probability to accept Snew if COST(Snew) > COST(Sinit)
  T slowly decreases to form the final solution
Boltzmann acceptance criterion, where r is a random number [0,1)
Simulated Annealing

## Slide 63: 3.5.3 Simulated Annealing
63
Simulated Annealing
Generate an initial solution and evaluate its cost
Generate a new solution by performing a random walk
Solution is accepted or rejected based on a temperature parameter T
Higher T indicates higher probability to accept a solution with higher cost
T slowly decreases to form the finalized solution.
Boltzmann acceptance criterion:
                currsol : current solution
                nextsol: new solution after perturbation
                T: current temperature
                r: random number between[0,1) from normal distr.

## Slide 64: 3.5.3 Simulated Annealing – Algorithm

## Slide 65: 3.5.3 Simulated Annealing – Algorithm
Input: initial solution init_sol
Output: optimized new solution curr_sol
T = T0 // initialization
i = 0
curr_sol = init_sol
curr_cost = COST(curr_sol)
while (T > Tmin)
while (stopping criterion is not met)
i = i + 1
(ai,bi) = SELECT_PAIR(curr_sol) // select two objects to perturb
trial_sol = TRY_MOVE(ai,bi) // try small local change
trial_cost = COST(trial_sol)
cost = trial_cost – curr_cost
if (cost < 0) // if there is improvement,
curr_cost = trial_cost // update the cost and
curr_sol = MOVE(ai,bi) // execute the move
else
r = RANDOM(0,1) // random number [0,1]
if (r < e –Δcost/T) // if it meets threshold,
curr_cost = trial_cost // update the cost and
curr_sol = MOVE(ai,bi) // execute the move
T = α ∙ T // 0 < α < 1, T reduction
© 2022 Springer Verlag

## Slide 66: 3.6 Pin Assignment
3.1 Introduction to Floorplanning
3.2 Optimization Goals in Floorplanning
3.3 Terminology
3.4 Floorplan Representations
  3.4.1 Floorplan to a Constraint-Graph Pair
  3.4.2 Floorplan to a Sequence Pair
  3.4.3 Sequence Pair to a Floorplan
3.5 Floorplanning Algorithms
  3.5.1 Floorplan Sizing
  3.5.2 Cluster Growth
  3.5.3 Simulated Annealing
  3.5.4 Integrated Floorplanning Algorithms
3.6 Pin Assignment
3.7 Power and Ground Routing
  3.7.1 Design of a Power-Ground Distribution Network
  3.7.2 Planar Routing
  3.7.3 Mesh Routing

## Slide 67: 3.6 Pin Assignment
During pin assignment, all nets (signals) are assigned to unique pin locations such that the overall design performance is optimized.
Pin Assignment
90 Pins
90 Pins
90 Connections
90 Pins
90 Pins
© 2022 Springer Verlag

## Slide 68: 3.6 Pin Assignment – Example
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards
Given: Two sets of pins
(1) Determine the circles

## Slide 69: 3.6 Pin Assignment – Example
(2) Determine the points
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards

## Slide 70: 3.6 Pin Assignment – Example
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards
(2) Determine the points

## Slide 71: 3.6 Pin Assignment – Example
(3) Determine initial mapping
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards

## Slide 72: 3.6 Pin Assignment – Example
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards
(3) Determine initial mapping and (4) optimize the mapping (complete rotation)

## Slide 73: 3.6 Pin Assignment – Example
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards
(3) Determine initial mapping and (4) optimize the mapping (complete rotation)

## Slide 74: 3.6 Pin Assignment – Example
(4) Best mapping (shortest Euclidean distance)
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards

## Slide 75: 3.6 Pin Assignment – Example
Final pin assignment
Koren, N. L.: Pin Assignment in Automated Printed Circuit Boards
(4) Best mapping

## Slide 76: 3.6 Pin Assignment
m
H. N. Brady, “An Approach to Topological Pin Assignment”, IEEE Trans. on CAD 3(3) (1984), pp. 250-255
B
B
m
l’
m
B
m
Pin assignment to an external block B

## Slide 77: 3.6 Pin Assignment
H. N. Brady, “An Approach to Topological Pin Assignment”, IEEE Trans. on CAD 3(3) (1984), pp. 250-255
Pin assignment to two external blocks A and B
a
b
lm~a
lm~b
d1
d2
d3
m
m
a1
a2
a3
a4
a5
a6
a7
a8
b1
b2
b3
b4
b5
b6
b7
b8
d1~d2
d3~d3
d2~d1
a
b
a1
a2
a3
a4
a5
a6
a7
a8
b1
b2
b3
b4
b5
b6
b7
b8

## Slide 78: 3.7 Power and Ground Routing
3.1 Introduction to Floorplanning
3.2 Optimization Goals in Floorplanning
3.3 Terminology
3.4 Floorplan Representations
  3.4.1 Floorplan to a Constraint-Graph Pair
  3.4.2 Floorplan to a Sequence Pair
  3.4.3 Sequence Pair to a Floorplan
3.5 Floorplanning Algorithms
  3.5.1 Floorplan Sizing
  3.5.2 Cluster Growth
  3.5.3 Simulated Annealing
  3.5.4 Integrated Floorplanning Algorithms
3.6 Pin Assignment
3.7 Power and Ground Routing
  3.7.1 Design of a Power-Ground Distribution Network
  3.7.2 Planar Routing
  3.7.3 Mesh Routing

## Slide 79: 3.7 Power and Ground Routing
Trunks connect rings to each other or to top-level power ring
Power and ground rings per block or abutted blocks
V
G
G
V
V
V
V
G
G
G
V
V
G
V
V
V
G
G
G
Power-ground distribution for a chip floorplan
© 2022 Springer Verlag

## Slide 80: 3.7 Power and Ground Routing
Hamiltonian path
GND
VDD
Planar routing
© 2022 Springer Verlag

## Slide 81: 3.7 Power and Ground Routing
Planar routing
Step 1: Planarize the topology of the nets
  As both power and ground nets must be routed on one layer, the design should be split using the Hamiltonian path
Step 2: Layer assignment
  Net segments are assigned to appropriate routing layers
Step 3: Determining the widths of the net segments
  A segment’s width is determined from the sum of the currents from all the cells to which it connects

## Slide 82: 3.7 Power and Ground Routing
Planar routing
GND
VDD
Generating topology of the two supply nets
Adjusting widths of the segments with regard to their current loads

## Slide 83: 3.7 Power and Ground Routing
Mesh routing
Step 1: Creating a ring
  A ring is constructed to surround the entire core area of the chip, and possibly individual blocks.
Step 2: Connecting I/O pads to the ring
Step 3: Creating a mesh
  A power mesh consists of a set of stripes at defined pitches on two or more layers
Step 4: Creating Metal1 rails
  Power mesh consists of a set of stripes at defined pitches on two or more layers
Step 5: Connecting the Metal1 rails to the mesh

## Slide 84: 3.7 Power and Ground Routing
Mesh routing
Ring
Mesh
Connector
Pad
Power rail
© 2022 Springer Verlag

## Slide 85: 3.7 Power and Ground Routing
Mesh routing
16
16
16
VDD rail
GND rail
Metal1
Via1
Metal2
Via2
Metal3
Via3
Metal4
VDD Metal4 mesh
GND Metal4 mesh
M1-to-M4 connection
Metal1 rail
1 Metal4 mesh
1 Metal5 mesh
2 Metal6 mesh
Metal4
Via4
Metal5
Via5
Metal6
M4-to-M6 connection
Metal6
Via6
Metal7
Via7
Metal8
M6-to-M8 connection
4 Metal7 mesh
4 Metal8 mesh
© 2022 Springer Verlag

## Slide 86: Summary of Chapter 3 – Objectives and Terminology
Traditional floorplanning
  Assumes area estimates for top-level circuit modules
  Determines shapes and locations of circuit modules
  Minimizes chip area and length of global interconnect
Additional aspects
  Assigning/placing I/O pads
  Defining channels between blocks for routing and buffering
  Design of power and ground networks
  Estimation and optimization of chip timing and routing congestion
Fixed-outline floorplanning
  Chip size is fixed, focus on interconnect optimization
  Can be applied to individual chip partitions (hierarchically)
Structure and types of floorplans
  Slicing versus non-slicing, the wheels
  Hierarchical
  Packed
  Zero-deadspace

## Slide 87: Summary of Chapter 3 – Data Structures for Floorplanning
Slicing trees and Polish expressions
  Evaluating a floorplan represented by a Polish expression
Horizontal and vertical constraint graphs
  A data structure to capture (non-slicing) floorplans
  Longest paths determine floorplan dimensions
Sequence pair
  An array-based data structure that captures the information
  contained in H+V constraint graphs
  Makes constraint graphs unnecessary in practice
Floorplan sizing
  Shape-function arithmetic
  An algorithm for slicing floorplans

## Slide 88: Summary of Chapter 3 – Algorithms for Floorplanning
Cluster growth
  Simple, fast and intuitive
  Not competitive in practice
Simulated annealing
  Stochastic optimization with hill-climbing
  Many details required for high-quality implementation (e.g., temperature schedule)
  Difficult to debug, fairly slow
  Competitive in practice
Pin assignment
  Peripheral I/Os versus area-array I/Os
  Given "ideal locations", project them onto perimeter and shift around, while preserving initial ordering
Power and ground routing
  Planar routing in channels between blocks
  Can form rings around blocks to increase current supplied and to improve reliability
  Mesh routing